## Slide 1: Framework of Operations, Administration and Maintenance (OAM) features for DetNet draft-ietf-detnet-oam-framework
Greg Mirsky
Fabrice Theoleyre
Georgios Papadopoulos
Carlos Bernardos
IETF-111, July 2021

## Slide 2: Updates
Many thanks to Balázs Varga and Pascal Thubert for their comments and thought-inspiring discussions
Bi-weekly calls discussing DetNet OAM – thanks to Janos for leading
The most significant updates in sections:
  Terminology
  Role of OAM in DetNet – DetNet sub-layers
  Information Collection – in-band methods to generate OAM information; in-band or out-of-band methods to collect OAM information
  Fault Localization and Characterization
  Requirements -
2

## Slide 3: Terminology
DetNet OAM domain: a DetNet network used by the monitored DetNet flow. A DetNet OAM domain (also referred to in this document as "OAM domain") may have MEPs on its edge and MIPs within.
DetNet OAM instance: a function that monitors a DetNet flow for defects and/or measures its performance metrics. Within this document, a shorter version, OAM instance, is used interchangeably.
Maintenance End Point (MEP): an OAM instance that is capable of generating OAM test packets in the particular sub-layer of the DetNet OAM domain.
In-band OAM - an active OAM is considered in-band in the monitored DetNet OAM domain when it traverses the same set of links and interfaces receiving the same QoS and Packet Replication, Elimination, and Ordering Functions (PREOF) treatment as the monitored DetNet flow.
Out-of-band OAM is an active OAM whose path through the DetNet domain is not topologically identical to the path of the monitored DetNet flow, or its test packets receive different QoS and/or PREOF treatment, or both.
On-path telemetry can be realized as a hybrid OAM method. The origination of the telemetry information is inherently in-band as packets in a DetNet flow are used as triggers. Collection of the on-path telemetry information can be performed using in-band or out-of-band OAM methods.
3

## Slide 4: OAM role in DetNet
MEP selection and placement – DetNet sub-layers
Re-use existing OAM tools – Echo Request/Reply
Address DetNet-specific scenario – PREOF in DetNet service sub-layer
4

## Slide 5: DetNet OAM requirements
Clearer separation between uni-directional and bi-directional OAM methods. For example, for a bi-directional OAM in DetNet the downstream MUST be in-band while upstream OAM MAY be out-of-band.
A new requirement on monitoring resources, e.g., buffer utilization, scheduler transmission calendar, allocated for the particular DetNet flow.
5

## Slide 6: Next steps
draft-varga-detnet-service-sub-layer-oam – an important element of the DetNet OAM
  Include the requirements for the Service sub-layer OAM in the draft
  Analyze the existing OAM to address the Service sub-layer OAM requirements – new work outside the scope of the draft
Continue bi-weekly discussions on DetNet OAM and the framework draft in particular
Your comments, suggestions are always welcome
WG LC
Thank you
6